## Slide 1: Modeling of Production and Logistics Systems
Lectures
Jan Fábry
5/13/2022

## Slide 2
Contents
Basic terms of production systems
  Basic model of production system
  Management concepts and types of production systems
  Forecasts
  Phases of production systems analysis
Models of designing production systems
  Product designing
  Placement of facilities
  Product schedule
Models of management of production systems
  Management of production systems
  Production planning
  Production scheduling
  Basic terms
  Production scheduling models
  Single machine scheduling models
  Extensions of basic single machine scheduling model
  Parallel machine models
  Flow shop scheduling
Computer simulation
  Introduction to computer simulation
  Data anlysis

## Slide 3: Basic terminology of production systems
1

## Slide 4
Basic terminology of production systems
Basic model of production system
3E strategy
  Economy
  Efficiency
  Effectiveness
Efficiency
  𝑧=𝑇𝑅−𝑇𝐶 𝑇𝑅=𝑝𝑞 𝑇𝐶=𝐹𝐶+𝑉𝐶 𝑉𝐶=𝑣𝑞 𝑧=𝑝𝑞−(𝐹𝐶+𝑣𝑞)=(𝑝−𝑣)𝑞−𝐹𝐶
Inputs
Efficiency
Production Processes
Economy
Effectiveness
Outside Environment
Outputs

## Slide 5
Basic terminology of production systems
STEEP analysis
  S = social
  T = technological
  E = economic
  E = ecological
  P = political
SWOT analysis
  S = strenghts
  W = weeknesses
  O = opportunities
  T = threats
Influence of external factors on the production system
Existing situation of the company in relation to its outside environment
Basic model of production system

## Slide 6
Basic terminology of production systems
Management concepts and types of production systems
Main functions of management
planning,
  decision making,
  organizing,
  leadership,
  control.
Development of managerial strategies
Production volume
Time
Cost
Quality
Speed
Present

## Slide 7
Basic terminology of production systems
Management concepts and types of production systems
Basic managerial conceptions
  JIT (Just-in-Time) – the required quantity at the required time.
  Lean Production System – elimination of useless processes, quality improvement.
  TOC (Theory of Constraints) – elimination of bottlenecks, optimising throughput.
  TQM (Total Quality Management) – comprehensive quality management, benchmarking.
  QRM (Quick Response Manufacturing) – speeding up processes, shortening delivery times.
  TEI (Total Employee Involvement) – employee involvement in quality improvement.
  BPR (Business Process Reingeneering) – changing business processes to improve the competitiveness of the company.
  Agile Manufacturing – the aim is to respond quickly to customer needs.
  SCM (Supply Chain Management) – optimising supply chains.

## Slide 8
Basic terminology of production systems
Management concepts and types of production systems
Types of production systems
  Type of operations
        production operations – transformation of inputs into outputs, easier measurability of quality,
        non-production operations – providing services, closer contact with customers.
  Type of product
        production companies,
        service companies,
        companies providing products and services.
  Type of production
        production to stock – stock based on an estimate of expected orders,
        production to order (contract) – special customer requirements,
        assembly to order (contract) – a combination of both, the product is assembled according to a special order from stocked components.

## Slide 9
Basic terminology of production systems
Management concepts and types of production systems
Types of production systems
  Type of production
        job production - low repeatability, high variability,
        batch production - the same products are produced consecutively in a certain quantity (in a series),
        mass production - high level of repeatability, low level of variability.

## Slide 10
Basic terminology of production systems
Forecasts
Time
  short range forcasts (up to 1 year),
  medium range forcasts (1-5 years),
  long range forecasts (over 5 years).
Focus
  technological forecasts – estimation of technical and technological progress,
  economic forecasts – estimation of changes in values of basic economic indicators,
  forecasts of future demand.

## Slide 11
Basic terminology of production systems
Phases of production systems analysis
Designing production systems.
Management of production systems.
Measurement of production systems performance.
Improving the performance of production systems.

## Slide 12
Basic terminology of production systems
Phases of production systems analysis
Designing production systems
  Product designing – what will be produced?
  Process designing – how will it be produced?
        selection of technology,
        capacity planning
        long-term planning – high capital expenditures,
        short-term planning – efficient use of existing equipment,
        the location of the facilities – where the facilities will be placed,
        the schedule of the facilities – the selection of the way of processing the products on the facilities
        fixed position of the product (house, bridge, aircraft),
        schedule by process (contract production),
        schedule by product (batch production),
        group (cell) schedule – grouping of facilities with similar operations.

## Slide 13
Basic terminology of production systems
Phases of production systems analysis
Management of production systems
Aggregate planning
Detailed planning
Multi-level planning
Determining batch sizes
Scheduling batches
Production management
Estimation of demad
Process 1
Process 2
Process 3
Outputs
Inputs
Demand (Order)
Process 1
Process 2
Process 3
Outputs
Inputs
Inside demand
Inside demand
Inside demand
  Management strategy
        PUSH
        PULL
Estimation of demad
Process 1
Process 2
Process 3
Outputs
Inputs

## Slide 14
Basic terminology of production systems
Phases of production systems analysis
Measurement of production systems performance
  Indicators
        Economy – resource costs.
        Efficiency – productivity (ratio of outputs to inputs), efficiency of resource involvement.
        Effectiveness – quality of outputs:
        Financial indicators – costs arising from poor quality or its prevention.
        Operational indicators – percentage of rejects, size of waste, delivery delays.
        Customer indicators – customer satisfaction.
Improving the performance of production systems
  Change of production system
        Reengineering – step (jump) change of performance.
        Kaizen – continuous improvement of performance – method PDCA (Plan, Do, Check, Act), Deming cycle.

## Slide 15: Models of designing production systems
2

## Slide 16
Models of designing production systems
Product designing
Objectives of company
  to bring new products to market as quickly as possible,
  increase the level of customer satisfaction, improve quality (TQM)
  reduce costs.
Means for designing
  using standards,
  Quality Function Deployment (QFD),
  collaborative designing.

## Slide 17
Models of designing production systems
Product designing
Using standards
  VDA (Verband der Automobilindustrie),
  modular designing – grouping of components into modules (easy and quick replacement),
  CAD (Computer-Aided Design), CAM (Computer-Aided Manufacturing), CAE (Computer-Aided Engineering).
Quality Function Deployment (QFD)
  a method developed in Japan in the 1960s,
  the company develops and produces only what the customer expects,
  using a method known as the "house of quality",
  the advantages of
  deepening the orientation on customer,
  shortening the time of product development, reducing costs of development and production,
  motivating collaborators to work together,
  simplicity and clarity of the tool.

## Slide 18
Models of designing production systems
Product designing
Collaborative designing
  several designers are involved in the design process.
  structured process,
  a project with co-operative activities that can take place in the following relations:
  serial – the following in succession,
  parallel – can be performed simultaneously,
  interconnected – must be performed simultaneously,
  design structure matrix P:

## Slide 19
Models of designing production systems
Product designing
Collaborative designing
  co-operative networks,
  example of 6 designers:
A
D
C
Serial relation
Direct interactive relation
Undirected interactive
dialogue
B
F
E

## Slide 20
Models of designing production systems
Product designing
Analysis of information flows
  the objective is to identify co-operating subgroups of designers,
  boolean algebra can be used :
a | b | a b | a b
1 | 1 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0
a | b |  | 
1 | 1 | 1 | 1
1 | 0 | 1 | 0
0 | 1 | 1 | 0
0 | 0 | 0 | 0

## Slide 21
Models of designing production systems
Product designing
Analysis of information flows
  Relation between elements through m direct relations: :
  Relation matrix:
  Two types of subsets of elements:
  there is a mutual relation between elements,
  no mutual relation between elements exists.

## Slide 22
Models of designing production systems
Product designing
Analysis of information flows
  Strong relation matrix S:
  The matrix is symmetric and transitive.
  The matrix can be rearranged into a matrix with a block-diagonal structure.
  Designers in the block interact to each other.

## Slide 23
Models of designing production systems
Product designing
Analysis of information flows
  Example
A
B
C
D
E
F
 | A | B | C | D | E | F
A | 0 | 1 | 0 | 0 | 0 | 0
B | 0 | 0 | 1 | 1 | 0 | 0
C | 0 | 1 | 0 | 0 | 0 | 0
D | 0 | 0 | 0 | 0 | 1 | 0
E | 0 | 0 | 0 | 0 | 0 | 1
F | 0 | 0 | 0 | 1 | 0 | 0
 | A | B | C | D | E | F
A | 0 | 1 | 0 | 0 | 0 | 0
B | 0 | 0 | 1 | 1 | 0 | 0
C | 0 | 1 | 0 | 0 | 0 | 0
D | 0 | 0 | 0 | 0 | 1 | 0
E | 0 | 0 | 0 | 0 | 0 | 1
F | 0 | 0 | 0 | 1 | 0 | 0
 | A | B | C | D | E | F | 
A | 0 | 1 | 1 | 1 | 1 | 1 | 
B | 0 | 1 | 1 | 1 | 1 | 1 | 
C | 0 | 1 | 1 | 1 | 1 | 1 | 
D | 0 | 0 | 0 | 1 | 1 | 1 | 
E | 0 | 0 | 0 | 1 | 1 | 1 | 
F | 0 | 0 | 0 | 1 | 1 | 1 | 
 | A | B | C | D | E | F | 
A | 0 | 1 | 1 | 1 | 1 | 1 | 
B | 0 | 1 | 1 | 1 | 1 | 1 | 
C | 0 | 1 | 1 | 1 | 1 | 1 | 
D | 0 | 0 | 0 | 1 | 1 | 1 | 
E | 0 | 0 | 0 | 1 | 1 | 1 | 
F | 0 | 0 | 0 | 1 | 1 | 1 | 
 | A | B | C | D | E | F
A | 0 | 0 | 0 | 0 | 0 | 0
B | 0 | 1 | 1 | 0 | 0 | 0
C | 0 | 1 | 1 | 0 | 0 | 0
D | 0 | 0 | 0 | 1 | 1 | 1
E | 0 | 0 | 0 | 1 | 1 | 1
F | 0 | 0 | 0 | 1 | 1 | 1
 | A | B | C | D | E | F
A | 0 | 0 | 0 | 0 | 0 | 0
B | 0 | 1 | 1 | 0 | 0 | 0
C | 0 | 1 | 1 | 0 | 0 | 0
D | 0 | 0 | 0 | 1 | 1 | 1
E | 0 | 0 | 0 | 1 | 1 | 1
F | 0 | 0 | 0 | 1 | 1 | 1
A
B
C
D
E
F
Components of a strong connection

## Slide 24
Models of designing production systems
Placement of facilities
Distance of the facility from
  sources,
  customers,
  competitors,
  other parts of system.
Other factors
  market – demand and competition,
  material – transport, labour, energy, etc.,
  non-material – ecology, social attitudes, customer habits, etc.
Objectives
  Connection of the new equipment with the existing production system?
  How many types of products will the new facility produce?
  How many new facilities will be placed?

## Slide 25
Models of designing production systems
Placement of facilities
Methods for selection of location
  Break-even point analysis.
  Multiple criteria evaluation of alternatives.
  Method of gravity center.
  Facility location problem – modified transportation problem.
  Facilities location problem – quadratic assignment problem.

## Slide 26
Models of designing production systems
Placement of facilities
Break-even point analysis
  Equalization of total costs and total revenues (zero profit):
  The total revenue is identical for all locations, i.e. the selection depends only on the total cost:
  Selection of the location for given total production size 𝑞*:
.

## Slide 27
Models of designing production systems
Placement of facilities
Break-even point analysis
  Example
  Three potential locations for the new facility are given: A, B and C. The table shows the fixed costs in CZK per month and the variable costs in CZK per unit of production for each location.
  Select a location for a known production of 800 units.
  How does the selection of location depend on the production size in general?
Location |  | 
A | 25000 | 10
B | 10000 | 30
C | 15000 | 20
Location |  | 
A | 25000 | 10
B | 10000 | 30
C | 15000 | 20

## Slide 28
Models of designing production systems
Placement of facilities
Break-even point analysis
  Example – continued
  Total cost are shown in 1000 CZK, production size in 100 units.
50
40
30
20
10
0
1
2
3
4
5
6
7
8
9
10
11
12
13
TC
q
B
C
A
A
B
C

## Slide 29
Models of designing production systems
Placement of facilities
Multiple criteria evaluation of alternatives
  Locations are evaluated in terms of several criteria.
  Weighted Sum Approach (WSA):
  Evaluation of i–th alternative according to j–th criterion:
  for
  Weight of j–th criterion:
  for ,
  Weighted sum:

## Slide 30
Models of designing production systems
Placement of facilities
Multiple criteria evaluation of alternatives
  Example
  Three potential locations for the new facility are given: A, B and C. Each option is evaluated according to seven criteria. The table shows the scores for each option according to the criteria and the weight of the criteria. The company is to select the location with the highest multi-criteria score.
Location | Material | Wages | Water | Transport | Climate | Taxes | 
A | 100 | 80 | 60 | 50 | 40 | 60 | 60
B | 60 | 80 | 90 | 60 | 70 | 40 | 72
C | 50 | 70 | 80 | 80 | 50 | 70 | 69
Weights | 0,10 | 0,05 | 0,40 | 0,10 | 0,20 | 0,15 | 
Location | Material | Wages | Water | Transport | Climate | Taxes | 
A | 100 | 80 | 60 | 50 | 40 | 60 | 60
B | 60 | 80 | 90 | 60 | 70 | 40 | 72
C | 50 | 70 | 80 | 80 | 50 | 70 | 69
Weights | 0,10 | 0,05 | 0,40 | 0,10 | 0,20 | 0,15 | 

## Slide 31
Models of designing production systems
Placement of facilities
Method of gravity center
  Knowledge of existing network of parts of the system, i.e. coordinates of their locations:
  Placement of the new facility in the center of gravity of the grid with coordinates:
  Knowledge of transport volumes between facilities and the new facility:
  Weights:
  Coordinates of gravity center:
a for

## Slide 32
Models of designing production systems
Placement of facilities
Method of gravity center
  Example – continued
Gravity center without transport volumes: (6;6)
Weighted gravity center: (8,1;5,3)

## Slide 33
Facility location problem – modified transportation problem
  Set of m potential locations for new facilities:
  Set of n destinations (customers or internal customers):
  Transportation costs:
  Variables:
Models of designing production systems
Placement of facilities
capacity of the facility in location
fixed cost for the use of location
demand of destination
amount of product transported from the facility placed in location to destination
shipping cost for transport a unit from source to destination

## Slide 34
Facility location problem – modified transportation problem
  Mathematical model:
Models of designing production systems
Placement of facilities

## Slide 35
Models of designing production systems
Placement of facilities
Facility location problem – modified transportation problem
  Example
  The company can use seven potential warehouses from which to transport material to its five production sites. The table gives the monthly requirements of the production sites and the monthly capacities of the warehouses (in thousands of tons). If a warehouse is used, the company has to pay the amounts indicated for its monthly rent (in thousands of euros). In addition, unit shipping costs (in euro per ton) are charged for each transport from warehouse to production site. Decide which warehouses to lease and how much material to transport between the leased warehouses and the manufacturing plants so that the total monthly cost is minimal.

## Slide 36
Facility location problem – quadratic assignment problem
  Set of n facilities:
  Set of n locations (workplaces):
  Variables:
Models of designing production systems
Placement of facilities
material flow between facilities and
distance between locationsand

## Slide 37
Facility location problem – quadratic assignment problem
  Mathematical model:
Models of designing production systems
Placement of facilities

## Slide 38
Facility location problem – quadratic assignment problem
  Linearization of mathematical model:
Models of designing production systems
Placement of facilities
,

## Slide 39
Models of designing production systems
Placement of facilities
Facility location problem – quadratic assignment problem
  Example
  The company intends to build 5 warehouses in 5 cities. In the first table the distances (in km) between the cities are given, in the second table the number of drives that must be made between the warehouses in one month. The aim is to decide which warehouse will be set up in which city in order to minimize the total transportation costs.

## Slide 40
Basic terms and notation
  Batch and mass production.
  Each product requires the same sequence of operations.
  The operations take place on facilities arranged in a production line.
  All input parameters are integer values.
Models of designing production systems
Product schedule
soperations,
duration of -th operation (
set of operations realized on -th workplace (
takt time,
precedence relation, -th operations precedes -th operation (
number of unused (idle) time units on the whole line,
number of unused (idle) time units on -th workplace (.

## Slide 41
Basic terms and notation
  Product workload
  Sum of durations of opertions on 𝑗-th workplace
Models of designing production systems
Product schedule

## Slide 42
Feasible schedule
  Example
  On a production line with 3 workplaces, where the product is produced, 8 operations with the following operation times (in min) have to be scheduled: 2,1,7,3,6,5,4,2. The 7th operation in the sequence with the duration of 4 min has to be scheduled after the operation with the duration of 1 min, i.e. the precedence relation 2 → 7 is valid. Takt time was set to 10 min.
  What is the product worlkoad?
  Decide, whether the following schedule is feasible:
  Determine a number of idle minutes on the production line.
  What is the production line efficiency?
Models of designing production systems
Product schedule

## Slide 43
Feasible schedule
  Conditions for a feasible schedule
  All operations must be scheduled
  Each operation must be assigned to exactly one workplace
  All operation assigned to a workplace must be done in takt time
  All precedence constraints must be satisfied
Models of designing production systems
Product schedule

## Slide 44
Optimal schedule
  Criteria
  Minimization of a number of workplaces for given value of takt time
  Minimization of takt time for given number of workplaces
  Minimization of idle time on the whole production line
  Maximization of the production line efficiency
Models of designing production systems
Product schedule

## Slide 45
Minimization of a number of workplaces
  Generally:
  For :
  For :
  If a takt time is given c = const., then
Models of designing production systems
Product schedule

## Slide 46
Minimization of a number of workplaces
  Example
  The company wants to schedule a product on the line, the production consists of 6 operations with durations (in min): 2,4,6,3,5,3. There are no technological interdependencies between the operations, i.e. no precedence relation is defined. The takt time is set to 8 min.
  What is a product workload?
  Determine minimal and maximal number of workplaces on production line and find any feasible schedule.
  For found schedule, determine a number of idle minutes on the whole production line and calculate its efficiency.
Models of designing production systems
Product schedule

## Slide 47
Minimization of takt time
  Generally:
  For :
  For :
  For :
  Theoretically achievable minimum takt time:
Models of designing production systems
Product schedule

## Slide 48
Minimization of takt time
  Highest possible takt time at which required production size 𝑄 can be achieved in working period of legth 𝑇:
  Realized takt time:
Models of designing production systems
Product schedule

## Slide 49
Minimization of takt time
  Example
  The company wants to schedule a product with 5 operations and their durations (in min): 5,1,3,4,2 on 3 workplaces. There is no precedence relation between the operations.
  What is the theoretically achievable minimum takt time?
  Find a feasible schedule for this value.
  What is the production line efficiency?
  How do the takt time and the production line efficiency change for durations: 2,2,2,5,4?
Models of designing production systems
Product schedule

## Slide 50
Minimization of takt time
  Example
  The company plans to achieve the daily production size 𝑄=100 units in the working period of length 𝑇=9 hours. Production of the product consists of 7 operations with durations (in min): 2,4,5,4,3,1,2.
  What is the highest possible takt time at which the desired daily production can still be achieved?
  Is it possible to find a feasible schedule for this takt time with the existing 5 workplaces?
  What will be the efficiency of the whole production line?
Models of designing production systems
Product schedule

## Slide 51
Heuristic methods
  Problem definition
  Production is divided into operations.
  The sequence of operations is given by precedence relations. For their graphical representation, a directed graph can be used.
  For each operation its duration is given.
  Total daily production size is required.
  Length of working period is .
Models of designing production systems
Product schedule

## Slide 52
Heuristic methods
  General procedure
  Step 1
  Calculate maximal takt time:
  Step 2
  Calculate product workload and theoretical minimal number of workplaces:
  Step 3
  Use one of 4 rules to assign operations to individual workplaces (see below).
  Step 4
  Calculate the production line efficiency:
Models of designing production systems
Product schedule

## Slide 53
Heuristic methods
  Rules for the assignment of operations to workplaces (see step 3):
  longest duration,
  maximal number of predecessors,
  maximal number of successors,
  maximal weight:
  where is a set of all immediate successors of -th operation.
Models of designing production systems
Product schedule

## Slide 54
Heuristic methods
  Example
  The company plans to produce 12 units of product per day, which production consists of 6 operations. All precedence relations are illustrated by the directed graph in the figure.
Models of designing production systems
Product schedule

## Slide 55
Heuristic methods
  Example – continued
  The table specifies the duration of each operation. In addition, the sets of the immediately preceding and immediately following operations are obtained from the graph. For further calculation, the numbers of all preceding and all following operations are additionally determined in the table for each activity. The length of the daily working period is 6 hours.
Models of designing production systems
Product schedule

## Slide 56
Mathematical model
Models of designing production systems
Product schedule

## Slide 57: Models of management of production systems
3

## Slide 58
Steps of management od production systems
  Production planning – determination of production capacity in the long term.
  Production scheduling – the schedulling of production to individual facilities over a shorter time horizon.
  Production control – implementation of schedules, done in real time.
Models of management of production systems
Management of production systems

## Slide 59
Planning of aggregated production
  Satisfaction of demand.
  Demand size is determined in aggregated units → production size is also determined in aggregated units.
  Assessment of production capacities and their possible increase.
Models of management of production systems
Production planning
Demad forecasts
Business plan
Product mix determination
Determination of resource availability
Setting up a supply chain

## Slide 60
Planning of aggregated production
  Decision-making problem
  Strategies for setting of control variables:
  Constant level. We do not change and, therefore, neither . There may be overproduction (higher storage costs) or underproduction (lost profits) relative to demand.
  Tracking strategy. Responding to the size of demand by changing workforce level so that production size matches the change in the size of demand as closely as possible. Higher costs associated with firing and hiring workers.
  Combined strategy. Partial tracking of demand size to use both approaches.
Models of management of production systems
Production planning
size of aggregated demand in period ,
production size in period ,
level of human resources (workforce) in period ,
inventory level in period .
Control variables

## Slide 61
Planning of aggregated production
  Mathematical model
Models of management of production systems
Production planning
number of groups into which the products are sorted (),
number of periods into which the time horizon is divided (),
demand forecast for products group in periods ,
number of source types (),
capacity of the source of type in period ,
number of units of the source type required by the products group ,
inventory level of products group at the end of period ,
initial inventory level of products group ,
safety stock of products group at the end of period ,
unit holding cost for products group per time period,
production size for products group in period .

## Slide 62
Planning of aggregated production
  Mathematical model – continued
Models of management of production systems
Production planning

## Slide 63
Planning of aggregated production
  Mathematical model – extension for overloading sources
Models of management of production systems
Production planning
size of the overload of the source type in period ,
penalty for the overload of the source,

## Slide 64
Multi-level planning
  Techniques
  Input-output analysis
  Material Requirement Planning (MRP).
  Manufacturing Resource Planning (MRP II).
  Gozinto graph
  Nodes
  Inputs: material, semi-finished products.
  Outputs: semi-finished products, final products.
  Arcs (directed)
  Transformation of material and products.
  Arcs evaluation: number of the input units transformed to the output unit.
Models of management of production systems
Production planning

## Slide 65
Multi-level planning
  Input-output analysis
  Leontief model:
  Optimization model:
Models of management of production systems
Production planning
input-output matrix of coefficients (amount of -th input item necessary to produce a unit of -th output item),
vector of required size of final production,
vector of all production input and output values,
.

## Slide 66
Multi-level planning
  Input-output analysis
  Example
  The company produces two final products V1 and V2 in 20 and 30 units. Two types of materials M1 and M2 and semi-finished product P are used. Product structure is expressed by Gozinto graph. Calculate all production input and output values:
  Use the Leontief model.
  Use the optimization model.
Models of management of production systems
Production planning

## Slide 67
Multi-level planning
  Input-output analysis
  Example – continued
Models of management of production systems
Production planning

## Slide 68
Multi-level planning
  MRP
  MPS – Master Production Schedule
  Transformation of aggregated plan into detailed production plan.
  What will be produced, when and in what sizes (special products and capacity requirements during the considered time period are determined).
  BOM – Bill of Materials
  List of all materials, components and semi-finished products.
  Assembly tree of product structure (Gozinto graph).
  Inventory levels (stock), delivery times (lead times), orders, safety stock levels.
Models of management of production systems
Production planning

## Slide 69
Multi-level planning
  MRP
  Example
  For 1 unit of product V, 1 unit of material M1, 2 units of material M2 and 4 units of material M3 are required. The delivery times (DT, in weeks) for each material type and for product V (production time) are shown in the figure (Gozinto graph). Product V can start production when all the material is available. The company has to deliver 80 units of product V in week 4 and 160 units of product V in week 7. The initial inventory level is 50 units of product V, 50 units of material M1, 40 units of material M2 and 140 units of material M3. The objective is to plan the material requirements for the whole period so that the demand for product V is met.
Models of management of production systems
Production planning

## Slide 70
Multi-level planning
  MRP
  Example – continued
Models of management of production systems
Production planning

## Slide 71
Multi-level planning
  MRP
  Example – continued
Models of management of production systems
Production planning

## Slide 72
Basic terms
  Elements
  machines (processors): or
  jobs: or
  Model classification
  Number of machines
  single machine models,
  multiple machine models, machines are arranged in parallel or in series.
  Random consideration:
  deterministic models,
  stochastic (probabilistic) models.
  Knowledge of all jobs:
  static,
  dynamic.
Models of management of production systems
Production scheduling

## Slide 73
Basic terms
  Precedence constraints (relations)
  Expression of relationship between jobs during processing.
  means that processing of job can start after processing is completed.
  Precedence graph – graphical representation of all precedence relations in the problem.
Models of management of production systems
Production scheduling

## Slide 74
Basic terms
  Preemptions
  the division of a job into two or more time intervals with a time gap between them,
  it is allowed to interrupt the processing of a job at any point in time and continue processing on another machine,
  interruption of the job usually occurs after the completion of an ongoing operation.
  Idle period
  a time interval in which no job is processed, i.e. no operation is performed,
  the idle period may be planned (machines maintenance), it may occur due to inefficient balancing of the production line, it may be forced (failures).
  Schedule
  arrangement of jobs in time,
  Gantt chart is a graphical representation of the schedule of jobs on a time axis.
Models of management of production systems
Production scheduling

## Slide 75
Basic terms
  Models of network analysis (project management)
  a single job, called a project,
  operations are called activities,
  each activity runs on a separate machine,
  the relationship of activities can be expressed by a network,
  time and cost analysis of projects, scheduling of shared resources.
Models of management of production systems
Production scheduling

## Slide 76
Production scheduling models
  Notation in models
  Given parameters are denoted by lowercase characters.
  Variables and calculated values are denoted by uppercase characters.
  Parameters – for each job it is possible to set the following data
  Processing time of job If a job consists of several operations, their durations are known as well.
  Release time (ready time), it is the earliest time at which job can start its processing.
  Due time of job It is committed completion time. Completion a job after its due time is allowed, but then a penalty is incurred. When a due time must be met, it is referred to as a deadline.
  Weight of job to express it importance (e.g. unit cost or penalty for delay performed).
Models of management of production systems
Production scheduling

## Slide 77
Production scheduling models
  Feasible schedule
  No machine can process multiple jobs simultaneously.
  No job can be processed on multiple machines simultaneously.
  No job processing can start before its release time.
  All precedence relations must be respected for all jobs.
  Other conditions must be respected
  no interruption is allowed in processing,
  jobs must be processed on a special machine,
  due times must be respected as deadlines,
  etc.
Models of management of production systems
Production scheduling

## Slide 78
Production scheduling models
  Example
  Consider 6 jobs whose precedence graph is shown in the figure. Schedule these jobs on 2 parallel machines. The table shows the processing times of all jobs (in hours).
Models of management of production systems
Production scheduling

## Slide 79
Production scheduling models
  Example – continued
Models of management of production systems
Production scheduling
  3 idle periods
  1 idle period
time
time

## Slide 80
Production scheduling models
  Variables (calculated values)
  completion time of -th job,
  flow time determines time that -th job spends in system,
  lateness of job is a difference between completion time and due time,
  for earliness it is valid: ,
  for tardiness it is valid: ,
  tardiness of job ,
  if
  if .
  Optimal production schedule is such a feasible schedule, which minimizes selected criterion.
Models of management of production systems
Production scheduling

## Slide 81
Production scheduling models
  Criteria:
  Makespan is time all jobs will have been completed, i.e. completion time of last processed job
  Mean completion time
  Maximal flow time (makespan)
Models of management of production systems
Production scheduling

## Slide 82
Production scheduling models
  Criteria:
  Mean flow time
  Maximum lateness
  Mean lateness
Models of management of production systems
Production scheduling

## Slide 83
Production scheduling models
  Criteria:
  Maximum tardiness
  Mean tardiness
  Number of overdue jobs
Models of management of production systems
Production scheduling

## Slide 84
Production scheduling models
  Model classification
  system with single machine,
  system with m parallel machines,
  flow-shop system with m serial machines, all jobs are processed in the same order (production line in mass production),
  open-shop system, system with m serial machines, jobs are processed in any order,
  job-shop system, system with m serial machines, each job is processed in fix order, but this order can differ for each job (production to order/contract).
Models of management of production systems
Production scheduling
:

## Slide 85
Production scheduling models
  Model classification
  release times of jobs do not have to be zero,
  jobs processing can be interrupted,
  in the model precedence relations are defined,
  selected criterion.
Models of management of production systems
Production scheduling
:

## Slide 86
Single machine scheduling models
  Model 1||𝑍
  There is single processor in the system.
  There are jobs processed, each consists of one operation.
  Symbol 𝑍 represents generally any criterion.
  For each job processing time is given.
  Constraints:
  S1: At the beginning, all jobs are available, i.e. for each job ready time is .
  S2: There are no precedence relations between jobs.
  S3: Processing times of jobs are independent of the order of their processing.
  No interruptions of jobs are allowed, there are no idle times in the schedule.
  Notation means that -th job is processed in -th place in order of the schedule.
Models of management of production systems
Production scheduling

## Slide 87
Single machine scheduling models
  Model 1||
  All optimal schedules are equivalent.
  Criterion value (maximal flow time) is independent of the order of jobs in schedule:
  A mathematical model for considering all due times as deadlines:
Models of management of production systems
Production scheduling
tardiness of job
lateness of job

## Slide 88
Single machine scheduling models
  Model 1|| – continued
Models of management of production systems
Production scheduling
no job is overdue
at least one job is overdue

## Slide 89
Single machine scheduling models
  Model 1|| – continued
  Example
  Consider 5 jobs for which you know their processing time (in hours), their due time (in hours) and their relative importance in terms of weight (see table). The ready times for all jobs are zero.
Models of management of production systems
Production scheduling
Total tardiness of jobs = 5 hours
= 12 hours
time
Job

## Slide 90
Single machine scheduling models
  Model 1|| – continued
  Example – continued
Models of management of production systems
Production scheduling
Total tardiness of jobs = 1 hour
= 12 hours
Alternative optimal schedule
time
Job

## Slide 91
Single machine scheduling models
  Model 1||
  In the optimal schedule, the jobs are ordered in non-increasing sequence of their weights:
  Example – continued
Models of management of production systems
Production scheduling
= 1,2 hour
time
Job

## Slide 92
Single machine scheduling models
  Model 1||
  The following property gives the optimal schedule:
  Example – continued
Models of management of production systems
Production scheduling
= 5,8 hour
time
Job

## Slide 93
Single machine scheduling models
  Model 1||
  The following property gives the optimal schedule:
  Example – continued
Models of management of production systems
Production scheduling
= 4,2 hour
time
Job

## Slide 94
time
Single machine scheduling models
  Models 1|| and 1||
  In the optimal schedule, the jobs are ordered in non-decreasing sequence of their due times:
  Example – continued
Models of management of production systems
Production scheduling
= = 1 hour
tardy job
Job

## Slide 95
Single machine scheduling models
  Models 1|| and 1||
  Lawler's algorithm (optimization approach)
  Step 1
  Calculate a value representing the total processing time of all jobs:
  Set of unscheduled jobs is
  Step 2
  This step is about finding a job that will be scheduled to end at time
  For this purpose, first calculate value for all jobs not yet scheduled:
  , for criterion ,
  , for criterion ,
  From all values calculated in this way, find the minimum value that corresponds to job :
Models of management of production systems
Production scheduling

## Slide 96
Single machine scheduling models
  Models 1|| and 1|| – continued
  Lawler's algorithm – continued
  Step 3
  Job is scheduled to end at time tj.
  Modify the value of and the set of unscheduled jobs:
  If or also then the optimal schedule is found, otherwise go to step 2.
Models of management of production systems
Production scheduling

## Slide 97
Single machine scheduling models
  Models 1|| and 1|| – continued
  Example – continued
Models of management of production systems
Production scheduling
= 0,2 hours
time
Job
Use of Lawler‘s algorithm for model 1||

## Slide 98
Single machine scheduling models
  Model 1||
  The following property gives the optimal schedule:
  Example – continued
Models of management of production systems
Production scheduling
= -1,8 hour
time
Job

## Slide 99
Single machine scheduling models
  Model 1||
  The following property gives the optimal schedule :
  Example – continued
Models of management of production systems
Production scheduling
= -3,5 hour
time
Job

## Slide 100
Single machine scheduling models
  Model 1||
  Moore's algorithm (optimization approach)
  Step 1
  Make the schedule using the following property:
  Jobs in this order are sequenced into . For overdue jobs the following set is introduced: .
  Step 2
  If sequence does not contain any overdue job, then sequence extended by jobs from set (in any order of jobs) generates optimal schedule .
  Number of overdue jobs is , algorithm ends.
Models of management of production systems
Production scheduling

## Slide 101
Single machine scheduling models
  Model 1|| – continued
  Moore's algorithm – continued
  Step 3
  In sequence , find the first overdue job. Let it be job on the place of the order.
  Among the first jobs, find job with the longest processing time:
  Move job from sequence to set and goto step 2.
Models of management of production systems
Production scheduling

## Slide 102
time
Single machine scheduling models
  Model 1|| – continued
  Example – continued
  The first (and the only one) overdue job is , which is on the 4th palce in sequence . Among the first 4 jobs, job has the longest processing time, therefore it is erased from sequence and it is added to set . Because in modified sequence no job is overdue anymore, the algorithm ends.
Models of management of production systems
Production scheduling
= (D2, D3, D1, D4, D5)
= (D2, D3, D4, D5, D1),
N = 1.
Job

## Slide 103
Extensions of basic single machine scheduling model
  Model 1
  Ready times of jobs do not have to be zero (release of condition S1).
  Jobs can be interrupted.
  Example
  Consider 3 jobs for which we know the processing times, ready times and due times (all values are in hours).
Models of management of production systems
Production scheduling
Job

## Slide 104
Extensions of basic single machine scheduling model
  Model 1 – continued
  Example – continued
  Schedule without an interruption, = 2/3 hour
  Schedule without an interruption, = 1/3 hour
  Schedule with the interruption, = 0 hour
Models of management of production systems
Production scheduling
time
time
time
Job

## Slide 105
Extensions of basic single machine scheduling model
  Model 1
  Technological dependence of jobs, expressed by means of precedence relations (release of condition S2).
  Extension of Lawler's algorithm (optimization approach).
  Step 1
  Calculate a value representing the total processing time of all jobs:
  Set of unscheduled jobs is
  Step 2
  This step is about finding a job that will be scheduled to end at time .
  Let set contain jobs that have no successors or which successors are already scheduled, i.e. there is no job which is their successor.
  For all jobs in set then calculate value
  From all values calculated in this way, find the minimum value that corresponds to job :
Models of management of production systems
Production scheduling

## Slide 106
Extensions of basic single machine scheduling model
  Model 1 – continued
  Extension of Lawler's algorithm – continued
  Step 3
  Job is scheduled to end at time tj.
  Modify the value of and the set of unscheduled jobs:
  If or also then the optimal schedule is found, otherwise go to step 2.
Models of management of production systems
Production scheduling

## Slide 107
Extensions of basic single machine scheduling model
  Model 1 – continued
  Example
  Make a schedule for 6 jobs, given by the precedence graph. The table shows the processing times of the jobs and their due times (both values are in hours).
Models of management of production systems
Production scheduling
Optimal schedule:
= 2 hour

## Slide 108
Extensions of basic single machine scheduling model
  Model 1
  The setup times of jobs depends on their order in the schedule (release of condition S3):
  setup time for start of processing job 𝑘 immediately following realization of job 𝑗.
  The problem of finding the optimal schedule can be transformed into the problem of finding the jobs order that minimizes the total time of all setups.
  Analogy with the travelling salesman problem, in which distances between locations correspond to setup times.
Models of management of production systems
Production scheduling

## Slide 109
Extensions of basic single machine scheduling model
  Model 1 – continued
  Mathematical model
Models of management of production systems
Production scheduling

## Slide 110
Extensions of basic single machine scheduling model
  Model 1 – continued
  Nearest neighbor algorithm (heuristic method)
  Step 1
  Select any job (suppose the processing begins and ends with job 1), denote it as . This job is included as the first job in the schedule, denoted as sequence . In this step, therefore .
  Total processing time of all jobs including setup times is denoted as . Set All other jobs create a set of not yet scheduled jobs .
  Step 2
  Find (among the jobs not yet scheduled) to job 𝑖 its "nearest neighbor", which is job 𝑘 with the minimal setup time:
Models of management of production systems
Production scheduling

## Slide 111
Models of management of production systems
Extensions of basic single machine scheduling model
  Model 1 – continued
  Nearest neighbor algorithm
  Step 3
  Include job at the end of sequence and exclude it form set . Modify the value of and replace index with index :
  If , go to step 4, otherwise go to step 2.
  Step 4
  Since, by assumption, the whole schedule ends by setup of the machine to job 1, modify the value of as follows:
  Algorithm ends, sequence corresponds to the feasible schedule, the value of equals to the total processing time of all jobs including all setup times in the schedule.
Production scheduling

## Slide 112
Models of management of production systems
Extensions of basic single machine scheduling model
  Model 1 – continued
  Example
  The company wants to schedule 8 jobs on 1 machine so that they are completed in minimum time. The table shows the job processing times and the setup times between jobs (all values are in minutes).
Production scheduling
Optimal schedule:
= (1,4,6,2,3,7,5,8),
= 447 min.
Nearest neighbor method:
= (1,8,6,3,7,5,2,4),
= 464 min.

## Slide 113
Models of management of production systems
Parallel machine models
  Model
  There are identical processors arranged in parallel in the system.
  There are jobs processed, each consists of one operation, there are no precedence relations between jobs.
  Ready times of all jobs are zero.
  Jobs can be interrupted after finishing the realized operation and can continue on the same or another machine.
  Notation means that -th job is processed in -th place in order of the schedule.
  For the minimal makespan it is valid:
Production scheduling
average occupancy time of machine
maximal processing time

## Slide 114
Models of management of production systems
Parallel machine models
  Model – continued
  McNaughton‘s algorithm (optimization approach)
  Step 1
  Calculate the value of . Assign job to machine at time 0.
  Step 2
  Assign (to the same machine) other jobs according to their ordinal numbers respecting .
  Three cases can occur:
All remaining jobs can be assigned to the machine, i.e. the last job assigned is job
Last assigned job is completed exactly on time
When job is assigned, the value of will be exceeded.
Production scheduling

## Slide 115
Models of management of production systems
Parallel machine models
  Model – continued
  McNaughton‘s algorithm – continued
  Step 3
  Next, we proceed according to which case occurred in the previous step:
All jobs are scheduled, the algorithm ends.
Assign job to the next machine at time 0 and go to step 2.
Split job so that its first part will be completed on the scheduled machine at time and assign its remaining part to the next machine at time 0, go to step 2.
  This procedure can lead to a maximum of interruptions.
Production scheduling

## Slide 116
Models of management of production systems
Parallel machine models
  Model – continued
  Example
  The problem is to schedule 10 jobs on 4 machines so that they are processed in minimum time, i.e. the makespan will be minimal. The table shows the processing times of the jobs (in min). The operations that make up each job have a duration of 1 min, so all jobs can be interrupted at any time after each minute of processing.
Production scheduling

## Slide 117
time
Models of management of production systems
Parallel machine models
  Model – continued
  Example – continued
  Calculate
  Since the jobs can only be interrupted after the completion of the operation currently being performed, it is necessary to calculate the ceiling, i.e. 11 min, from the value 43/4.
Production scheduling
=
real interruptions of jobs

## Slide 118
Models of management of production systems
Parallel machine models
  Model – continued
  Mathematical model for obtaining the schedule without the interruption of jobs (if it exists)
Production scheduling
The objective is not necessary to obtain a feasible schedule

## Slide 119
Models of management of production systems
Parallel machine models
  Model – continued
  Example – continued
Production scheduling
time

## Slide 120
Models of management of production systems
Parallel machine models
  Model
  Jobs cannot be interrupted.
  Generalization of the mathematical model formulated for the model
  is a variable, not a calculated constant, it is necessary to set integrality constraints (due to the continuity of operations in the job).
  The objective is
  Jobs cannot be interrupted.
  NP-hard problem.
Production scheduling

## Slide 121
Models of management of production systems
Parallel machine models
  Model – continued
  Example
  The problem is to schedule 10 jobs on 4 machines so that they are processed in minimum time, i.e. the makespan will be minimal. The table shows the processing times of the jobs (in min). The operations that make up each job have a duration of 1 min, so all jobs can be interrupted at any time after each minute of processing.
Production scheduling

## Slide 122
Models of management of production systems
Parallel machine models
  Model – continued
  Example – continued
Production scheduling
time

## Slide 123
Models of management of production systems
Parallel machine models
  Model – continued
  Heuristic algorithm:
  Step 1
  Make the schedule using the following property:
  Step 2
  Select first jobs in the sequence from step 1 and assign them to machines at time 0.
  Step 3
  Select next job in the sequence and assign it after the last job to the machine, which is released first, i.e. after the job, which of all the last jobs on the machines ends first.
  Repeat this process until all jobs are scheduled.
Production scheduling

## Slide 124
Models of management of production systems
Parallel machine models
  Model – continued
  Example – continued
Production scheduling
time

## Slide 125
Models of management of production systems
Parallel machine models
  Model
  The same principle as the optimization procedure for the model :
  Step 1
  Make the schedule using the following property :
  Step 2
  Select first jobs in the sequence from step 1 and assign them to machines at time 0.
  Step 3
  Select next job in the sequence and assign it after the last job to the machine, which is released first, i.e. after the job, which of all the last jobs on the machines ends first.
  Repeat this process until all jobs are scheduled.
Production scheduling

## Slide 126
Models of management of production systems
Parallel machine models
  Model – continued
  Example – continued
Production scheduling
= 6,3 min
time

## Slide 127
Models of management of production systems
Flow shop scheduling
  Model
  There are serial machines in the system.
  There are jobs processed, each consists of operations, each of them is processed on one machine.
  The jobs must be processed on the machines in the same order, i.e. 𝑖-th operation of each job is processed on 𝑖 -th machine.
  Processing time of -th operation of -th job is denoted as
  No machine can process more than one job at a time, and no job can be processed on multiple machines simultaneously.
Production scheduling

## Slide 128
Models of management of production systems
Flow shop scheduling
  Model – continued
  Constraints:
  S1 : Ready times for all jobs and machines are 0.
  S2 : There are no precedence relations between jobs.
  S3 : Processing times of jobs are independent of the order of their processing on the machine.
  S4 : Operations cannot be interrupted.
Production scheduling

## Slide 129
Models of management of production systems
Flow shop scheduling
  Model – continued
  Example
  Find a feasible schedule for 5 jobs that need to be scheduled on 3 serially arranged machines. The table contains the job processing times (in min) on each machine.
Production scheduling

## Slide 130
Models of management of production systems
Flow shop scheduling
  Model – continued
  Example – continued
  Feasible schedule:
Production scheduling
time

## Slide 131
Models of management of production systems
Flow shop scheduling
  Model – continued
  Johnson‘s algorittm (optimization approach) for the problem with 2 machines
  Step 1
  Set of jobs is split to two subsets:
  Step 2
  Order jobs in set to the non-decreasing sequence () of operation processing times . Order jobs in set to the non-increasing sequence () of operation processing times .
  Step 3
  Optimal jobs schedule () on both machines consists of sequence () followed by sequence (). Value is given by the completion time of the last job in sequence () on the second machine.
Production scheduling

## Slide 132
Models of management of production systems
Flow shop scheduling
  Model – continued
  Example
  Let 6 jobs be given, which must be scheduled to 2 serially arranged machines. The table shows the processing times (in min) of the jobs on both machines. The objective is to minimize the completion time of all batches.
Production scheduling

## Slide 133
Models of management of production systems
Flow shop scheduling
  Model – continued
  Example – continued
  Step 1
  Step 2
  Step 3
Production scheduling
.
,
=15.
time

## Slide 134: Computer simulation
4

## Slide 135
Computer simulation
Definition
  Representation of a real (but also planned, not yet existing) system with its stochastic and dynamic processes in the form of a simulation model.
  The basic idea is to simulate the behaviour of a real system through a simulation model and, based on experimentation with this model, to propose changes that will improve the functioning of the system.
Areas of application of computer simulation
  Optimization of large-scale production systems.
  Analysis of logistics processes inside a company or within the entire supply chain.
  Optimization of warehousing processes.
  Optimization of production scheduling.
  Improvement of communication systems, optimization of information flows.
Introduction to computer simulation

## Slide 136
Computer simulation
Costs associated with computer simulation
  Staff costs for a qualified analyst and programmer.
  Costs associated with managers' time spent communicating with the analyst during the project.
  The cost of powerful computing equipment (HW).
  Costs for software.
  Data collection costs.
Introduction to computer simulation

## Slide 137
Computer simulation
Simulation project
  Problem recognition and goals setting.
  Creation of a conceptual model (CM).
  Data collection and analysis.
  Creation of a simulation model (SM).
  Verification and validation of the model (checking whether the SM is consistent with the original CM and whether the SM is in compliance with the reality).
  Performing experiments.
  Analysis of results.
  Creation of project documentation.
  Implementation of results.
Introduction to computer simulation

## Slide 138
Computer simulation
Basic analytical tools
  tables,
  diagrams,
  charts,
  schemes.
General methods of processing data
  Clustering – the goal is to sort the data into groups (clusters) so that the elements of each group share a common attribute (car type, car-body type, color).
  Filtering – selection of elements that meet the specified conditions (simple filters, multiple filters).
  Sorting - sorting data according to the values of one or more attributes (the so-called key), the result is the order of elements.
  Pairing - combining information (character values) from several databases or lists obtained, for example, on the basis of passing products through individual check points.
Data analysis

## Slide 139
Computer simulation
Software
  Access, Excel, SAS, SPSS, Gretl, Statgraphics, MATLAB, R.
Statistical data analysis
  (Random) Experiment – an experiment that can be repeated and the outcome of which is not known in advance.
  Random variable – variable whose value is given by the result of an experiment (discrete, continuous).
  (Random) Event – the result of an experiment expressed by the value of a random variable. .
  Probability of a random event – numerical expression of the degree of possibility of occurrence of a random event.
  Probability distribution –a rule that assigns to each value or interval of values the probability that a random variable will take on that value or a value from that interval.
Data analysis

## Slide 140
Computer simulation
Statistical data analysis
  Random number is defined as the value of a uniform probability distribution on the interval (0, 1). Several generators have been developed to generate random numbers, the most commonly used of which are arithmetic generators. Random numbers are obtained by calculating each number using some arithmetic operation from the previous number. Since this is an arithmetic calculation and not a random operation, numbers obtained in this way can only be described as pseudo-random numbers. The random numbers generated are then transformed by various methods into values of random variables.
  The inverse transformation method is one of the methods used to convert a random number 𝑟 into values of a random variable 𝑋. Example for values of a uniform probability distribution on the interval
Data analysis
cumulative distribution function on the interval ,
random number,
value of random variable with uniform probability distribution.

## Slide 141: Thank you for attention
Jan Fábry
Department of Production, Logistics and Quality Management
fabry@savs.cz www.janfabry.cz